## Slide 2
-Land used as truckstand, but no road signs
-No safety for pedestrian

## Slide 3
-Roadside are occupied by illegal shopkeepers
-Nonmotorized vehicle is parked
-In this road bike take wrong way for changing side

## Slide 4
-Semi motorized and non motorized vehicle reduce the capacity of highway
-This vehicles are stopped in intersection for parking or taking passenger, create bottleneck
Do not have any clear position for placing any sign
Road marker are faded away

## Slide 5
-Existing Road alignment is not proper
-U turn create bottleneck and cause of accident in this intersection

## Slide 6
-Pre-School is ahead, but no Warning signs anywhere
- Wrong Land use. High number of Pedestrian cross the road for taking vehicle of opposite direction, But there is no zebra crossing
- There is no speed bumper though there is a pre-school ( Though speedbumper reduce mobility of the highway, but it increase safety for the childrens)

## Slide 7
- Madrasa is ahead, But no warning sign
- Pedestrian cross the road all the time.
- Vehicle often take u turn here, but no proper warning, and less visibility due to tree of the median

## Slide 8
Non-motorized vehicle use the highway, which create bottleneck

## Slide 9
Road markers are faded

## Slide 10
- Truck are parked in the both side of this highway, which increase road friction

## Slide 11
- It is very surprising nowhere warning sign is used before any school/college, though it is a national highway.
- Land use is wrong
- Students cross the road always, but there is no zebra crossing.( Safety vs mobility paradox)

## Slide 12
Iland is not clear.

## Slide 14
This road do not maintain standard cross section, no-drainage, water-logging issue occur after rain

## Slide 16
buses are blocking the road, used as busstand
illegal parking, shop , creating side friction
Roads are not access controlled

## Slide 18
the design of road divider is not good, not visible from a distance

## Slide 19
Improper placement of Electric-pol will create fatal crash in highway
temporary storage is the middle of the highway may cause fatal crash

## Slide 20
Sides of the bridges should have enough footpath in this location

## Slide 21
Construction work is going on, but no warning sign