## Slide 3
Road median should not be sharp at start
road side are being used as parking, increasing side friction
semi motorized vehicle use this spot for pickup and dropping passenger.
road marker is faded

## Slide 4
footpath is occupied for illegal parking and as a result pedestrian are using road

## Slide 5
electric poll on the top of road may cause fatal crash

## Slide 7
footpath are occupied by homeless people
Not a pedestrian friendly footpath
electric poll on the top of road

## Slide 8
illegal shops, create side friction
high volume of pedestrian , but no zebra crossing

## Slide 9
road marking is not visible , so imaginary road marking is provided

## Slide 10
No sign for driver About this T section

## Slide 13
- Electric polls are directly on the road
- Roadside marker faded

## Slide 14
- All the electric polls are in bad position, hazard
- Road markers are faded, washed away

## Slide 16
this road is not visible from a distance, no warning sign
Roadside markers faded

## Slide 19
the alignment of the roundabout is not proper

## Slide 22
- road marker are not visible, faded away
- no drainage system exist